;; LD-BYTES
L0556: INC D ; reset the zero flag without disturbing carry.
        EX AF,AF' ; preserve entry flags.
        DEC D ; restore high byte of length.
        DI ; disable interrupts
        LD A,$0F ; make the border white and mic off.
        OUT ($FE),A ; output to port.
        LD HL,L053F ; Address: SA/LD-RET
        PUSH HL ; is saved on stack as terminating routine.
        IN A,($FE) ; read the ear state - bit 6.
        RRA ; rotate to bit 5.
        AND $20 ; isolate this bit.
        OR $02 ; combine with red border colour.
        LD C,A ; and store initial state long-term in C.
        CP A ; set the zero flag.

;; LD-BREAK
L056B: RET NZ ; return if at any time space is pressed.

;; LD-START
L056C: CALL L05E7 ; routine LD-EDGE-1
        JR NC,L056B ; back to LD-BREAK with time out and no edge present on tape.
        LD HL,$0415 ; set up 16-bit outer loop counter for approx 1 second delay.

;; LD-WAIT
L0574: DJNZ L0574 ; self loop to LD-WAIT (for 256 times)
        DEC HL ; decrease outer loop counter.
        LD A,H ; test for
        OR L ; zero.
        JR NZ,L0574 ; back to LD-WAIT, if not zero, with zero in B.
        CALL L05E3 ; routine LD-EDGE-2
        JR NC,L056B ; back to LD-BREAK if no edges at all.

;; LD-LEADER
L0580: LD B,$9C ; set timing value.
        CALL L05E3 ; routine LD-EDGE-2
        JR NC,L056B ; back to LD-BREAK if time-out
        LD A,$C6 ; two edges must be spaced apart.
        CP B ; compare
        JR NC,L056C ; back to LD-START if too close together for a lead-in.
        INC H ; proceed to test 256 edged sample.
        JR NZ,L0580 ; back to LD-LEADER while more to do.

;; LD-SYNC
L058F: LD B,$C9 ; initial timing value in B.
        CALL L05E7 ; routine LD-EDGE-1
        JR NC,L056B ; back to LD-BREAK with time-out.
        LD A,B ; fetch augmented timing value from B.
        CP $D4 ; compare
        JR NC,L058F ; back to LD-SYNC if gap too big, that is a normal lead-in edge gap.
        CALL L05E7 ; routine LD-EDGE-1
        RET NC ; return with time-out.
        LD A,C ; fetch long-term mask from C
        XOR $03 ; and make blue/yellow.
        LD C,A ; store the new long-term byte.
        LD H,$00 ; set up parity byte as zero.
        LD B,$B0 ; timing.
        JR L05C8 ; forward to LD-MARKER
        ; the loop mid entry point with the alternate
        ; zero flag reset to indicate first byte is discarded.

;; LD-LOOP
L05A9: EX AF,AF' ; restore entry flags and type in A.
        JR NZ,L05B3 ; forward to LD-FLAG if awaiting initial flag which is to be discarded.
        JR NC,L05BD ; forward to LD-VERIFY if not to be loaded.
        LD (IX+$00),L ; place loaded byte at memory location.
        JR L05C2 ; forward to LD-NEXT

;; LD-FLAG
L05B3: RL C ; preserve carry (verify) flag in long-term state byte.Bit 7 can be lost
        XOR L ; compare type in A with first byte in L.
        RET NZ ; return if no match e.g. CODE vs DATA.
        LD A,C ; fetch byte with stored carry
        RRA ; rotate it to carry flag again
        LD C,A ; restore long-term port state.
        INC DE ; increment length ??
        JR L05C4 ; forward to LD-DEC. but why not to location after ?

;; LD-VERIFY
L05BD: LD A,(IX+$00) ; fetch byte from memory.
        XOR L ; compare with that on tape
        RET NZ ; return if not zero.

;; LD-NEXT
L05C2: INC IX ; increment byte pointer.

;; LD-DEC
L05C4: DEC DE ; decrement length.
        EX AF,AF' ; store the flags.
        LD B,$B2 ; timing.

;; LD-MARKER
L05C8: LD L,$01 ; initialize as %00000001

;; LD-8-BITS
L05CA: CALL L05E3 ; routine LD-EDGE-2 increments B relative to gap between 2 edges.
        RET NC ; return with time-out.
        LD A,$CB ; the comparison byte.
        CP B ; compare to incremented value of B.
        ; if B is higher then bit on tape was set.
        ; if <= then bit on tape is reset.
        RL L ; rotate the carry bit into L.
        LD B,$B0 ; reset the B timer byte.
        JP NC,L05CA ; JUMP back to LD-8-BITS
        LD A,H ; fetch the running parity byte.
        XOR L ; include the new byte.
        LD H,A ; and store back in parity register.
        LD A,D ; check length of
        OR E ; expected bytes.
        JR NZ,L05A9 ; back to LD-LOOP while there are more.
        LD A,H ; fetch parity byte.
        CP $01 ; set carry if zero.
        RET ; return in no carry then error as checksum disagrees.

;; LD-EDGE-2
L05E3: CALL L05E7 ; call routine LD-EDGE-1 below.
        RET NC ; return if space pressed or time-out.
        ; else continue and look for another adjacent
        ; edge which together represent a bit on the tape.

;; LD-EDGE-1
L05E7: LD A,$16 ; a delay value of twenty two.

;; LD-DELAY
L05E9: DEC A ; decrement counter
        JR NZ,L05E9 ; loop back to LD-DELAY 22 times.
        AND A ; clear carry.

;; LD-SAMPLE
L05ED: INC B ; increment the time-out counter.
        RET Z ; return with failure when $FF passed.
        LD A,$7F ; prepare to read keyboard and EAR port
        IN A,($FE) ; row $7FFE. bit 6 is EAR, bit 0 is SPACE key.
        RRA ; test outer key the space. (bit 6 moves to 5)
        RET NC ; return if space pressed. >>>
        XOR C ; compare with initial long-term state.
        AND $20 ; isolate bit 5
        JR Z,L05ED ; back to LD-SAMPLE if no edge.
        LD A,C ; fetch comparison value.
        CPL ; switch the bits
        LD C,A ; and put back in C for long-term.
        AND $07 ; isolate new colour bits.
        OR $08 ; set bit 3 - MIC off.
        OUT ($FE),A ; send to port to effect change of colour.
        SCF ; set carry flag signaling edge found within time allowed.
        RET ; return.